## Slide 1: An Overview of the Epidemic of Bus Fires
BISC West – July 19, 2016
Joseph Peoples
Vehicle Fire Consultant
busfireguy@gmail.com
919 608-3878

## Slide 2
SEPT 2005
Fire engulfs vehicle carrying seniors from Houston area nursing home
23 deaths

## Slide 3
20 people die after Germany bus fire
November 2008
A fire department official, Claus Roehrbein, said: "Passengers who were sitting close to the exit could get away, but the others had no chance."
Police suspect the blaze was caused by a passenger sneaking a cigarette in the coach toilet.
It is thought that some of the elderly passengers who perished had walking disabilities and were unable to escape in time.

## Slide 4
47 people died and 34 were injured.
According to a suicide note found in his home, the man was unhappy with his life and had decided to light the fire to vent his anger.
An express bus burst into flames on an elevated roadway in southeastern China
November 2008

## Slide 5
China tourist bus fire kills 30
local officials believed an oil leak caused by the crash may have sparked the fire.
June 2016

## Slide 6: What do these famous people have in common
Toby Keith
Lee Bryce
Miley Cyrus
Whoopi Goldberg
Wynonna Judd
Lady Antbellum

## Slide 7: 4. How do bus fires occur
Equipment Failure
Maintenance Issues
Design
Age of Bus
Accident/Collision
Arson
Flammable
Liquid/Gas
Friction
Electrical
Arc/Short
4. How do bus fires occur

## Slide 8: NEW risk considerations
EMMISSIONS
WEIGHT
NOISE
Euro I
Euro II
Euro III
Euro IV
Euro V
Euro VI
1992
2013
PLASTICS
INSULATION
DPF
?
HEAT
FUEL LOAD
Oxygen
5. Preventive fire safety

## Slide 9: The Fire Timeline (Stages)
INCIPIENT
SMOKE
FLAME
5. Preventive fire safety – FRA, Inspections, Improved processes
FIRE GROWTH
Detection
Suppression
Aging
Fuel
Heat
Premature Failure
AN increase of 10 ° above max temp can Shorten Hose life by half.
Turbocharger
Exhaust Components
Bearings (Friction)
Hydraulic Hoses
Electrical Cables/Loom
Air Cleaner Housing
Insulation/Sealants
Rubber Hoses
Bearings
Fuels/Lubricants
Mechanical Damage
?
How can we better prevent fires

## Slide 10: Fire Risk Management
Dispatch
911 Style Flipcards
Management Policy
-Highest level of safety
-Minimize Bus Fire Risks
-Meet or exceed safety objectives
Increase Concern
well-informed interest
Maintenance
Fire Causes
Risk Assessment
Best Practices
Drivers
Knowledge of early fire indicators
Passenger Safety
  Briefings
  Emergency Evacuations
Fire Actions
Increase Awareness
knowledge or perception
Baseline
monitor the effectiveness of safety risk controls

## Slide 11: Fire Risk Assessment
Highest level of safety practical Keep risks as low as reasonably practical
Hazard Areas
Engine Compartment
Luggage Compartment
Lavatory
Wheel wells
Improved Specifications
Temperature Rating
Training
Repair /Replacement Procedures
Emergency Exits
Firewalls/Fire Resistance methods
Fire Detection and Suppression
Fuel
Liquid/Gaseous
Solids (Plastics/Insulation)
Fire Risk Causes
Duty Cycle
Aging (temperature)
Mechanical Damage (abrasion)
Passenger injury/fatality
By-Products/Evacuation
Vehicle Damage $$$$$$
Growth and spread of fire
Likelihood
Consequence
Geometry, Clutter
Ventilation/Penetration
Ignition Sources
Turbocharger/Exhaust
Identify
Assess
Control

## Slide 12: The fire event
Detect
Control
Fire growth (engine/cooling fan)
  Shutdown Engine
  Shut Off Batteries
Safety of Passengers
Prevent introduction of toxic fumes
  Shutdown (HVAC)
Safely Stop Bus
Evacuate Passengers
Alert Driver
Acknowledge Risk
I SMELL SOMETHING BURNING
?
YOUR BUS IS ON FIRE
5. Preventive fire safety – Safety features

## Slide 13: Automatic detection and suppression
Detect
Control
Fire growth (engine/cooling fan)
Safety of Passengers
Shutdown (HVAC)
Prevent introduction of toxic fumes
Safely Stop Bus
Evacuate Passengers
Alert Driver
5. Preventive fire safety – Safety features
Shutdown Engine
Shut Off Batteries
Discharge Extinguisher

## Slide 14: Benefits
Safety of Passengers
Safely Stop Bus
Evacuate Passengers
Alert Driver
Shutdown (HVAC)
Shutdown Engine
Shut Off Batteries
Discharge Extinguisher
ALLOW THE DRIVER TO FOCUS ON THE SAFETY OF THE PASSENGERS
AUTOMATIC FIRE SUPPRESSION SYSTEMS REMOVE THE HUMAN FACTOR
5. Preventive fire safety – Safety features

## Slide 15: Are Fire Suppression Systems Effective
Components
harsh environments
Required maintenance
Detection
Fast Detection with minimal nuisance alarms
Suppression
Sufficient qty of extinguishing agent and nozzzles
Re-Ignition Protection
Effective during all operation modes (high airflow, low airflow)

## Slide 16: Voluntary certification - Fire suppression systems
Common platform for securing minimum level of safety and security
Tested in a well-defined and objective way with realistic fire hazards that can occur on a bus based on sound science
Components tested for harsh environments to secure survivability
Ensures good distribution and amount of suppression agent
Re-igntition protection
Repeatable and reproducible
5. Preventive fire safety – Safety features

## Slide 17: 3. Current and upcoming regulations
3. Current and upcoming regulations

## Slide 18
“Extinguishing systems shall be provided in buses with combustion engine placed behind the driver: “
Regulation 34 liquid fuel tanks.
Regulation 43 plastic safety glazing
Regulation 44 materials of child restraint systems
Regulation 67 LPG
Regulation 100 electric power train of vehicles, including fuel cells
Regulation 110 CNG and/or LNG
Regulation 118 burning behavior of interior materials
Regulation 122 heating systems, in particular combustion heaters
Regulation 107 uniform provisions with regard to general construction
Based on the European bus directive 2001/85/EC
  No flammable or liquid-absorbing sound-proofing materials in engine compartment.
  Heat-resistant partitioning between engine compartment and rest of the bus.
  Safe construction and installation of cables.
  Fusing.
  Isolating switch for circuits with a voltage exceeding 100 V.
  Safe and accessible installation of the battery.
  Space provided for fire extinguishers and first-aid kits.
  No flammable materials within 10 cm of any potential heat source, such as exhaust systems or high voltage equipment for example.
  Number of Doors
  Size of Seats
  Rear View Mirrors
  Wheelchair Places
  Evacuation Routes
  (Automatic Extinguishing Systems)

## Slide 19: Summary
Bus fires – a common issue world wide
Preventive fire safety
- Reduction of loss of buses
- Securing business continuity
- Enhancing goodwill
More research is needed
Isolated events seldom lead to a fire… but more often the combination of several events. Experience should be used for prevention not as a lesson
7. Summary

## Slide 20: 4th International Conference on Fires in Vehicles - FIVE 2016
Event partner:
Honorary Sponsors:
October 5-6 2016
Baltimore, MD
www.firesinvehicles.com
Casey C. Grant
Executive Director, The Fire Protection Research Foundation
Thomas Littleton
Associate Administrator for Transit Safety and Oversight, Federal Transit Administration (FTA)
Mike Weston
Director of Buses, Transport for London
Jonas Brandt
SP Technical Research Institute of Sweden
Key Note Speakers