## Slide 1
BUSINESS BOUND

## Slide 2: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
What does safety and maintenance have in common ?
Where do our roles and responsibilities overlap ?
49CFR and 29CFR

## Slide 3: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
49CFR FMCSA Regulations
Mechanic Certifications – Annual Inspections and Brake Certification
DVIRs
Work Orders
PM Inspections
Deferred maintenance
90 Safety checks for windows and escape hatches
Roadside Inspection Documentation
Maintenance Records relating to DOT Reportable Crashes
ADA equipment
Intermediary between maintenance and operations

## Slide 4: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
INSPECTOR QUALIFICATIONS
Certification – 49 CFR – Part 396.19
Motor carriers are responsible for ensuring that individual(s) performing an annual inspection under 396.19 are qualified as follows:
□ Understands the inspection criteria set forth in Part 393 and Appendix G and can identify defective components
□ Is knowledgeable of and has mastered the methods, procedures, tools and equipment used when performing an inspection
□ ls capable of performing an inspection by reason of experience, training, or both, and qualifies in one of the following categories (check all that apply):
I. □ Successfully completed a State or Federal training program or has certificate from a State or Canadian Province which qualifies the person to perform commercial vehicle safety inspections. Specify:
or
II. □ Have a combination of training or experience totaling at least one year as follows (check all that apply): A. □ Participation in a truck manufacturer-sponsored training program or similar commercial training program designed to train students in truck operation and maintenance. Where and Date:
B. □ ______ (years) experience as a mechanic or inspector in a motor carrier maintenance program. Name and Date:
C. □ ______ (years) experience as a mechanic or inspector in truck maintenance at a commercial garage, fleet leasing company, or similar facility. Name of Facility and Dates: D. □ ______ (years) experience as a commercial vehicle inspector for a State,
Provincial, or Federal Government. Where and Dates:
I certify the above information is true and accurate to the best of my knowledge.
Employee ________________________________________ _______________
Motor Carrier/Company _________________________________ _______________
Evidence of Inspector Qualifications are on file at:

## Slide 5: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
BRAKE INSPECTOR QUALIFICATIONS
Certification – 49 CFR – Part 396.25
“Brake Inspector” means any employee of a motor carrier who is responsible for ensuring all brake inspections, maintenance, service, or repairs to any commercial motor vehicle, subject to the motor carrier’s control, meet the applicable Standards.
No motor carrier shall require or permit any employee who does not meet minimum brake inspector qualifications to be responsible for the inspection, maintenance, service or repairs of any brakes on its commercial motor vehicles.
Minimum Qualifications
□ Understands and can perform brake service and inspection
□ Is knowledgeable of and has mastered the methods, procedures, tools and equipment necessary to perform brake service and inspection
□ Is capable of performing brake service or inspection by reason of experience, training, or both, and qualifies in one of the following categories (check all that apply):
I. Has successfully completed an apprenticeship program sponsored or approved by a State, Canadian Province, a Federal agency or labor union, or has a certificate from a State or Canadian Province which qualifies the person to perform brake service or inspections. Specify:
II. □ Has brake-related training or experience or a combination thereof totaling at least one year as follows (check all that apply):
A. □ Participation in a brake maintenance or inspection training program sponsored by a brake or vehicle manufacturer or similar commercial training program. Where and Date:
B. □ ______ (years) experience performing brake maintenance or inspection in a motor carrier maintenance program. Name and Date:
C. □ ______ (years) experience performing brake maintenance or inspection at a commercial garage, fleet leasing company, or similar facility. Name of Facility and Dates:
I certify the above information is true and accurate to the best of my knowledge.

## Slide 6: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
BRAKE INSPECTOR QUALIFICATIONS
Certification – 49 CFR – Part 396.25
I certify the above information is true and accurate to the best of my knowledge.
Employee __________________________________________ ______________
Motor Carrier/Company __________________________________ _____________ Evidence of Inspector Qualifications are on file at:
_____________________________________________________________________________
What about techs at other shops ?
Who is responsible for the recordkeeping ?

## Slide 7: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
DVIR
Defect only or daily reports defects or not
Paper or plastic ?
Record retention 90 days ? 6 months ?
Do you retain DVIRs with work orders
Reviewed for completeness?
Reviewed for repeat defects ?

## Slide 8: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
Work orders
Why is safety concerned with work orders?
If it’s not in writing it never happened…
Inspections, repairs, campaigns

## Slide 9: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
PM program
How is it structured?
Time , miles, hours … combinations
What are the requirements?
Federal, state may be more strict, manufacturer recommendations
How many inspections do you have?
Can they be made more efficient?

## Slide 10: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
Deferred maintenance
Definition ?
How do you monitor it ?
How do you measure it?
Who sets your maintenance schedules?
Who holds maintenance responsible?

## Slide 11: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
90 day window checks and escape exits
How are these monitored?
Make sure you cover all of the requirements
Markings, handles accessible, hatches open and close properly
Kids love to peel off the stickers on the windows as well as the seat backs
Great time to check seat belts and other safety equipment as well

## Slide 12: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
Roadside inspection documentation
Make sure they are all accounted for and returned to the reporting agency within 15 days
Some states are fining companies by the day for late returned reports
Make sure you have repair documentation for all defects
Review defects and especially OOS reports
DataQ any reports that you feel and can substantiate are incorrect
All of these inspections good and bad impact your safety rating

## Slide 13: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
Maintenance records for DOT reportable crashes
What is a recordable crash ?
Make sure everything from the tow bill to any inspections and repairs are documented and carefully filed with the accident file
Make sure everyone that does any inspection or repairs are qualified
Review maintenance records prior to crash as well

## Slide 14: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
ADA equipment
Check buses not only for lift operation but also the ability to move seats
Also check and record inspection of tie down equipment for all types of mobility devices
Set up a program with the maintenance shop to regularly run and test ADA lifts

## Slide 15: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
Intermediary between maintenance and operations
Develop a positive relationship with your shop and operations
Review policies in how many vehicles per day can be removed for maintenance
Work together to make a schedule to do maintenance prior to the busier seasons
Consider away trip inspections prior to multiday trips

## Slide 16: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
What are your responsibilities for safety in the shop
29 CFR OSHA regulations
Also check with your state to see if they have additional regulations
Forklifts
Storage and record keeping of HAZWOPER documents
Storage of hazmats
Monthly inspections
Pit and lift safety

## Slide 17: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
What are your responsibilities for safety in the shop
Safety covers every part of our operations
Become familiar with the OSHA laws
Managing by walking around
Look, talk, engage
Know what you are looking at
Ask questions and listen
Don’t be afraid to spend time in the shop

## Slide 18: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
29 CFR OSHA regulations
This the occupational safety code similar to the FMCSRs
Make sure you look at the non-construction aspects of the code
Simple items can costs lives and heavy penalty
Rule of 7s
Fire extinguishers, exit signs, PPE
Also check with your state to see if they have additional regulations
Many offer free classes to help you learn this aspect of safety

## Slide 19: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
Forklifts
Do you have one?
Is everyone trained to use it?
Are you doing daily inspections?
Are you performing or have contracted maintenance on it?
When is training required ?

## Slide 20: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
Storage and record keeping of HAZWOPER documents
MDS material data sheets
Explain all of the hazards associated with the item
Explains exposure hazards and how to handle releases
Work with local fire departments for hazmat awareness
Make sure your employees are trained on where they are and how to read them

## Slide 21: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
Storage of hazmats
Know what the regulations are
Know where they are
Know what and what not can be stored in close proximity
Know what kind of vessel they can be stored in
Many techs use old soda bottles ,etc to store simple chemicals for ease of use
Know what to do in case of a release

## Slide 22: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
Monthly inspections
Part of managing by walking around
Form a committee of different departments
Look at all aspects
Fire extinguishers, exit signs, PPE, guards on machines, lock out tag out
Document the inspections
Have a suggestion method for employees to report safety items or ideas to improve safety

## Slide 23: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
Pit and Lift Safety
Pits
Make sure they have protection barriers poles, lines , nets
Make sure they are clean
Check entrances and exits
Make sure anyone driving over a pit has a spotter
Make sure guide lines and all critical areas are painted and kept clean

## Slide 24: SAFETY DIRECTOR 101 THE ROLE OF SAFETY IN MAINTENANCE
Pit and Lift Safety
Lifts
Receive training from the lift manufacturer
Make sure all new employees are trained on the equipment

## Slide 25
Mike McDonal
mmcdonal@saucontech.com
410-245-5525